| Worksheet Revision No.: |  | Serial Number (SN): |  |
| --- | --- | --- | --- |
| Customer: |  |  |  |
| Project: |  | Completed by/Date: |  |
| SOR No.: |  | Quote No.: |  | Reviewed by/Date: |  |
| Model Number: | LKCO- | Complete System | System Item No.: |
| Spare Power Subrack (044591) SN | Spare Optical Subrack (047629) SN | Spare Compensation Module (047630) SN | Spare Optical Subsystem (047628) SN |
| Rectifier Control | Yes No | Calibration Point: | kA (e.g. 500kA) |

If calibration point is not specified, calibration will be at full-scale

| MAINS POWER : |
| --- |
| Voltage: | 115 Vac 230 Vac | Frequency: 50Hz 60Hz | Optional DC VDC (044877) |

STANDARD MEASUREMENT OUTPUTS :

Standard Feedback Current Output

1A Full Scale 30kA through 100kA

4mA/kA 130kA through 500kA

3.333mA/kA over 500kA

Standard Shunt Voltage Output   (Select one)

10mV/kA 30kA through 100kA

1mV/kA over 100kA                  or

1V Full Scale    Item No.       (See Table 1)

OPTIONAL MEASUREMENT OUTPUTS (Additional cost applies to all options):

Select up to three (3) of the following eight (8) optional outputs:

2nd Shunt Voltage (not available with heater option or some option combinations)    	SN      ___________

(Select one)   	1V Full Scale       Item No.       (See Table 1) or

1V =       kA   Item No.       (Contact DynAmp)

High Level Voltage –Isolated (0-10V) (047767)     SN      ___________

0 to      V / 0 to      kA measurement span

Low Level Current – Isolated  	 (047766)     SN      ____________

(Select one)	 0 to 20 mA  or   4 to 20 mA / 0 to      kA measurement span

2nd Low Level Current – Isolated 	(047766)      SN      ____________

(Select one)	 0 to 20 mA  or   4 to 20 mA / 0 to      kA measurement span

Table 1

Shunt Voltage Output

(1V Full Scale)

1V Full Scale      System         Shunt Output

Item Number

LKCO-15	044879

LKCO-30	044879

LKCO-45	044879

LKCO-60	044879

LKCO-80	044879

LKCO-100	044879

LKCO-130	045054

LKCO-155	045055

LKCO-180	045056

LKCO-225	045057

LKCO-260	045058

LKCO-300	045059

LKCO-350	045060

LKCO-400	045061

LKCO-450	045062

LKCO-500	045063

LKCO-550	045064

LKCO-600	045065

Modbus RTU *	(044448)    		SN      ____________

Modbus TCP *	(045152)     		SN      ____________

Profibus  *	(044449)     		SN      ____________

Frequency - Isolated  (044800) (0-25kHz)		SN      ____________

(Select one)       NPN (24V)   PNP (24V)   TTL (5V)      0 to      kA measurement span / 0 to      kHz

* Reports Measurement Level and Diagnostic Relay Status (on-off )

All form fields outlined or underlined in red are customer fill-in fields.

| DIGITAL DISPLAY OPTIONS : |  |
| --- | --- |
|  | Internal Digital Display (044446) | 4.5 Digit LED – AC Power SN ____________ |
|  | Internal Digital Display (045179) | 4.5 Digit LED – DC Power SN ____________ |
|  | Remote Digital Display (045937) | 4.5 Digit LED – AC Power SN ____________ |
|  | Remote Digital Display (045938) | 4.5 Digit LED – DC Power SN ____________ |

ENVIRONMENTAL :

|  | Minimum Ambient Temperature | Maximum Ambient Temperature |  |
| --- | --- | --- | --- |
| Measurement Head / Compensation Module | (F / (C | (F / (C |  |
| Metering Unit Enclosure (Options below) | (F / (C | (F / (C |  |
| Standard Cooling Fan (select voltage to match mains power) | 115 Vac (045605) | 230 Vac (045606) |
|  | DC power (045557) |  |
| * Optional Heater (required for ambient less than 14(F/-10(C ) | 115 Vac (044453) | 230 Vac (044454) |
| * Optional Air Conditioner (required for ambient over 104(F/ 40(C) | 115 Vac (044875) | 230 Vac (044876) |
| Note: * DC Mains option may require additional customer supplied AC power for environmental options |
| METER UNIT ENCLOSURE MOUNTING : |  |  |
| Wall Mount (standard) | Pedestal Option (044455) |

BUS BAR DIMENSIONS :

| Actual Bus Size | Measuring Head Centerlines |
| --- | --- |
| P1 = mm | mm (Calculated by DynAmp) |
| P2 = mm | mm (Calculated by DynAmp) |
| Bus Bar Orientation | Rise Run |
| Maximum Bus Temperature Rise (above 25(C) ______ (C at Bus Current _______kA |

MEASURING HEAD CONFIGURATIONS :

|  |  | The following additional information is required to complete the sensor design. Dimensioned ‘plan and elevation’ drawings of all bus work within 5m of each measuring head location. Drawings must have enough detail to fully represent the bus layout in X, Y & Z axis. Include any walls and columns in the immediate vicinity of the measuring head. Include photos to the extent possible. Indicate the maximum current and direction on the bus bars. |
| --- | --- | --- |

Remote Compensation Module

Location Letter (A,B,C,D,E,F,G,H)

Horizontal Vertical

Offset Distance “m”

| Sensor Fiber Length: (Calculated by DynAmp) | m |  |
| --- | --- | --- |
| Interconnection Cable Length: | m | (30m standard – additional cable per meter - 044989) |

| MEASURING HEAD MOUNTING : |  |  |
| --- | --- | --- |
| Wall (Standard) | Bus Bracket (044514) | Bus Suspension (044878) |

Number of Bus Brackets (determined by DynAmp) (044514)

OPTIONS : (from customer purchase order)

ACCESSORIES : (from customer purchase order)

Special System Tests or Configurations :

Special Requirements : (QA, Inspection, Shipping, etc.)

Additional costs / fees may apply to the following documents and services :

| Manuals Required Sets: | Quantity |  | (default is one) | (047631) |
| --- | --- | --- | --- | --- |
| Custom Manual Number | Quantity |  | Item No. |

|  | Printed w/Shipment | Via E-Mail | On CD ROM |  |
| --- | --- | --- | --- | --- |
| Addendum(s): |  |  |  | Item No(s). |
| Certificate of Calibration |  |  |  | Item No(s). |
| Certificate of Calibration - NIST |  |  |  | Item No(s). |
| Certificate of Origin: |  |  |  | Item No(s). |
| Certificate of Conformance/Compliance |  |  |  | Item No(s). |
| Certificate of Warranty: |  |  |  | Item No(s). |
| CE Certificate: |  |  |  | (044847) |
| Application / Site Information |  |  |  | (099912) |
| Engineering |  |  |  | (099913) |
| Other |  |  |  |  |  |
| Other |  |  |  |  |  |

| Note: All comments, corrections and changes must be initialed and dated. |  |
| --- | --- |